## Slide 1: Efficiency improvement in existing 80 t/h bagasse fired low pressure boiler
DESCON Engineering Limited
Sugar conference Sept. 12, 2011

## Slide 2
Mostly sugar mills produce out of each kg of bagasse 2 kg of MP steam.
This means an boiler efficiency of approx 71% (based on LHV value of 1850 kcal/kg.
However efficiency would be 83% based on:
30% excess air
25 C ambient temperature
no unburned losses.
No economizer
So, approx 12% of the available heat is lost.
This is mainly caused by:
high unburned losses
high excess air
Present situation

## Slide 3
Unequal air flow distribution over grate.
Preheated air
Grate bars
What are the root causes?
2 Low pressure drop of dumping grate due to large number of spaces between the grate bars.

## Slide 4
piling of ash and wet bagasse has high impact on air distribution over furnace area. Make air distribution more worse.
Pile size will only increase further and increase unburned.
Also over firing of grate bars is most likely to occur.
4. Unequal distribution of fuel over furnace area
Fuel spreading

## Slide 5
Over firing air
Over firing air
5. No overfiring.
Means: No proper mixing of unburned gasses and unburned fly ash leaving furnace.

## Slide 6
A solid and simple design
no mechanically moving elements
water cooled tubes as supporting structure connected with boiler natural circulation system
No special hopper required under grate
Due to absence of hopper less height required
Even air distribution over grate system by increased pressure drop and proper designed air distribution box
On line ash removal system. No interruption in steam supply
Air temperature can be far above 200 C. No limitation.
How to minimize those losses?
1. Apply a Water cooled inclined grate
Grate loading: 2,4 MW/m2
Excess air 30 till 40%
Unburned losses 3 till 4%

## Slide 7
Primary air
Preheated till 200 C min
blowing piping
Ash hopper
Supporting frame
Steam blow piping
Steam blow nozzles
Ash removal system

## Slide 8
Example of water cooled inclined grate with alloy plates no.1

## Slide 9
113 t/h medium pressure boiler in Jaimaca
Example of water cooled inclined grate with alloy plates no. 2

## Slide 10
Example of water cooled inclined grate with alloy plates No.3
In Brasil is said:
Watercooled pinhole grate, the best solution for bagasse firing for cogeneration in sugar mills

## Slide 11
ERK water cooled inclined grate system as all in one solution
In 80th specially designed by ERK for bark firing in Northern Europe.
Same grate system with small angle and steam cleaning is suitable for bagasse firing and other low ash biomass fuels

## Slide 12: Example ERK grate system Biomass 35t/h, 20bar, saturated

## Slide 13
2. Equalize fuel spreading over full grate
preheated air
Install a rotary wheel in spreading air line in order to fluctuate the amount of spreading air.
Further install separate fan for spreading with head of 70 mbar to improve spreading power

## Slide 14
3. Install over firing system in sidewalls
For proper mixing of all unburned particles and gasses with air.
Nozzles of larger size and high air velocity to create a deep penetration of air into the furnace.

## Slide 15
Water cooled inclined grate
If possible it should be set lower to get more time for burning out. Also feeders and overfiring
Wet ash removal
Additional baffles in hopper for improved air distribution
Over firing air
Nozzles in side wall
And new secondary fan of higher head
Overview of modifications
Equalizing fuel spreading

## Slide 16
Main Advantages of water cooled inclined pinhole grate:
Very low maintenance. No renewal of parts.
Automatic ash removal
Easy control for operators
Drying of bagasse for efficiency improvement is not limited by grate.
Fuel saving up to 8 %
Proven design over more then 20 years

## Slide 17: More efficiency improvement.
Install economizer at outlet boiler
Downstream the air pre-heater
Efficiency improvement 5 %.
Stack temperature decreased to 145 C.
Economizer of bare or finned tubes
Flue gas pressure drop increases with 4 mbar
Economizer.
Stack and ID fan relocated

## Slide 18
Do not install economizer upstream the air-preheater.
Why?
The space is limited, so only a small economizer can be installed.
Improvement in efficiency maximum 2,3 %.
The air temperature at outlet pre-heater drops from 200 C to 160 C.
Due to lower air temperature the firing of bagasse will get poor at high moisture content of bagasse.
the unburned losses will increase. This will have negative effect on efficiency
Limited space